## Slide 1
What the AI takes in, gives back, and how we use it
Hourly solar and wind generation for the next 24 to 48 hours, with an honest range around every number.
1 What goes in
Tomorrow's weather forecast: sunshine, cloud, wind speed and direction, temperature, humidity, pressure, rain.
Sun position and the calendar: hour, season, daylight.
What the plant produced up to now, never after.
How many hours ahead we are predicting.
No actual weather is ever used as input.
2 Physics + AI
Physics model: what a solar or wind plant should produce in this weather.
LightGBM (the AI): learns from history where the physics model is wrong and corrects it.
A weighted blend of the two, with weights set separately for near and far hours.
Ranges are then calibrated on a separate window so they hold up.
3 What comes out
For every hour, a range in MW instead of one number:
Median: the best guess
P10 to P90: 80% chance the real value lands inside
P5 to P95: the outer edges
A trust score from 0 to 100 for each hour.
4 How we use it
Alerts for low or high generation.
Battery and backup plan for the day.
Deviation-charge estimate (illustrative rates).
Trust score marks which hours to rely on.
Dashboard shows forecast against what happened.
On a test period the model never saw, the blend makes about 28% less error than the persistence baseline for solar (daylight) and 36% less for wind.
Real Open-Meteo weather, virtual digital-twin plant at a real location. All figures come from our evaluation harness.